## Slide 1: RUEDI Vendor Town Hall Meeting
4th July 2025

## Slide 2: Overview
RUEDI consist of two lines
  Imaging at 1.5MV and ns to ps timing at nm resolution
  Diffraction at 4.5MV with ca. 10fs timing
  Additional compute / sample support
Main areas for procurement
Electron Optical Components (x2)
Sample Stages
Detectors

## Slide 3: Schematic Outline
Prism
Quadrupole
pairs
Detectors
Diagnostics
Round lenses
X-Ray
EELS
CL1,2 CL3
OL
IL1,2
PL
1.5MV Static Accelerator
Electrostatic Chopper
1(a)
2 and 3
1(b)
4

## Slide 4: Schematic Outline
Prism
Quadrupole
Detector
Diagnostics
Round lens
X-Ray
EELS
1(a).
1(b).
2 and 3
4

## Slide 5
Basic Instrument Specification
1. Static Plane Wave Illumination for Phase and Diffraction Contrast TEM and
Selected Area Diffraction
2. Target Spatiotemporal Resolution 10-15 to 10-18 m.s (105 to 106 improvement over intermediate voltage instruments)
3. 1.5MV maximum voltage (10-6 ripple, beam chopper)
4. Large gap OL polepiece for a variety of in-situ sample holders
5. 4k x 4k pixel direct detector
6. Future options for scanning, EELS and EDX…
Notes: For the basic capability of imaging, we would state that the aim is 1 microsecond (10^-6 s) and 1 nanometer (10^-9 m) giving a combined spatiotemporal resolution of 10^-15 meter.seconds. This is ~100-000 x better than current microscopes. The goal for RUEDI if all goes well, would be to get to 10^-18 meter.seconds (1nm and 1 nanosecond or 1micron and 1 picosecond etc) and be 10^6 x better than current microscopes.

## Slide 6
1(a and b). Condenser and Projector Optics
3 x Condenser system, 3 x Intermediate / Projector system
  Power supplies included as part of procurement
  Deflectors, apertures and stigmators included as part of procurement
  Assembly on a rigid horizontal girder
Single or multiple vendors – lead vendor and subcontractors possible
Bids for both CL and PL systems or a combination
Staged procurement likely
Outline requirements available early 2026

## Slide 7
2. Objective Lens
Large Gap OL operating below saturation (weak CO field)
  Compatible with side entry goniometer
  Provision for laser entry
  Power supplies included as part of procurement
  Deflectors, apertures and stigmators included as part of procurement
Single or multiple vendors
Preference is for a lead vendor and subcontractors to include goniometry and vacuum
Staged procurement likely
Outline requirements available early 2026

## Slide 8
3. Sample Stages
Ultrafast Science, Global Impact
Cooling and Hating (with Biasing)
Gas Cells (with Heating)
Liquid Cells (flow and static)
Cryo (N2 and He)
Cryo Transfer
Single and Double Tilt
Tilt Rotate
Electrical and Optical feedthrough
Single or multiple vendors
Goniometer to be determined
Staged procurement likely
Outline requirements available end 2025

## Slide 9
4. Detectors
4k x 4k Pixels minimum
MAPS (thin) technology with radiation hardened pixels
Counting and integrating modes for single electron detection
Single Vendor (may include additional detectors for diagnostics)
10 year lifetime support of sensor and electronics
Initial technical requirements available end 2025